## Slide 1
Operations Management
Statistical Process Control
Regents Park Publishers
T2LM4

## Slide 2: Overview

## Slide 3: Three SQC Categories
Statistical quality control (SQC) is the term used to describe the set of statistical tools used by quality professionals
SQC encompasses three broad categories of;
  Descriptive statistics
    e.g. the mean, standard deviation, and range
  Statistical process control (SPC)
    Involves inspecting the output from a process
    Quality characteristics are measured and charted
    Helpful in identifying in-process variations
  Acceptance sampling used to randomly inspect a batch of goods to determine acceptance/rejection
    Does not help to catch in-process problems

## Slide 4: Traditional Statistical Tools
Descriptive Statistics include
  The Mean- measure of central tendency
  The Range- difference between largest/smallest observations in a set of data
  Standard Deviation measures the amount of data dispersion around mean
  Distribution of Data shape
    Normal or bell shaped or
    Skewed

## Slide 5: Distribution of Data
Normal distributions
Skewed distribution

## Slide 6: SPC Methods-Control Charts
Control Charts show sample data plotted on a graph with CL, UCL, and LCL
Control chart for variables are used to monitor characteristics that can be measured, e.g. length, weight, diameter, time
Control charts for attributes are used to monitor characteristics that have discrete values and can be counted, e.g. % defective, number of flaws in a shirt, number of broken eggs in a box

## Slide 7: Statistical Process Control Charts
Show when changes in data are due to:
  Special or assignable causes
    Fluctuations not inherent to a process
    Represents problems to be corrected
    Data outside control limits or trend
  Common causes or chance
    Inherent random variations
    Consist of numerous small causes of random variability

## Slide 8: Control Chart Basics
Process Average
UCL = Process Average + 3 Standard Deviations
LCL = Process Average – 3 Standard Deviations
UCL
LCL
+3σ
- 3σ
Common Cause Variation: range of expected variability
Special Cause Variation:
Range of unexpected variability
time

## Slide 9: Process Variability
Process Average
UCL = Process Average + 3 Standard Deviations
LCL = Process Average – 3 Standard Deviations
UCL
LCL
±3σ → 99.7% of process values should be in this range
time
Special Cause of Variation:
A measurement this far from the process average is very unlikely if only expected variation is present

## Slide 10: Statistical Process Control Charts
Statistical Process Control Charts
X(bar) charts and R-charts
c-charts
Used for measured numeric data
Used for proportions (attribute data)
Used for number of attributes per sampling unit
p-charts

## Slide 11: X(bar) chart and R-chart

## Slide 12: X(bar) chart and R-chart
Used for measured numeric data from a process
Start with at least 20 subgroups (samples) of observed values
Subgroups usually contain 3 to 6 observations each

## Slide 13: Steps to create an x-chart and an R-chart
Calculate subgroup means and ranges
Compute the average of the subgroup means and the average range value
Prepare graphs of the subgroup means and ranges as a line chart

## Slide 14: Steps to create an x-chart and an R-chart
Compute the upper and lower control limits for the x(bar)chart
Compute the upper and lower control limits for the R-chart
Use lines to show the control limits on the x(bar) and R-charts
(continued)

## Slide 15: Example: x-chart
Process measurements:
 |  |  |  |  | Subgroup measures | 
Subgroup number | Individual measurements |  |  |  | Mean, x | Range, R
1 2 3 … | 15 12 17 … | 17 16 21 … | 15 9 18 … | 11 15 20 … | 14.5 13.0 19.0 … | 6 7 4 …
 |  |  |  |  | Average subgroup mean = x | Average subgroup range = R

## Slide 16: Average of Subgroup Means and Ranges
Average of
subgroup means:
where:
xi = ith subgroup average
k = number of subgroups
Average of
subgroup ranges:
where:
Ri = ith subgroup range
k = number of subgroups

## Slide 17: Computing Control Limits
The upper and lower control limits for an x-chart are generally defined as
UCL = Process Average + 3 Standard Deviations
LCL = Process Average – 3 Standard Deviations

## Slide 18: Computing Control Limits
Since control charts were developed before it was easy to calculate σ, the interval was formed using R instead.

## Slide 19: Computing Control Limits
The value A2R is used to estimate 3σ , where A2 is given.
The upper and lower control limits are
(continued)
where A2 = Shewhart factor for subgroup size
A2 values are in the sample problems.

## Slide 20: Example: R-chart
The upper and lower control limits for an
R-chart are
where:
D4 and D3 are taken from the Shewhart table
for subgroup size = n
D4 and D3 values are in the sample problems.

## Slide 21: x-chart and R-chart
UCL
LCL
time
UCL
LCL
time
R-chart
x-chart

## Slide 22: p-Chart

## Slide 23: p-Chart
Control chart for proportions
  Is an attribute chart
Shows proportion of nonconforming items
  Example -- Computer chips: Count the number of defective chips and divide by total chips inspected
    Chip is either defective or not defective
    Finding a defective chip can be classified a “success”

## Slide 24: Creating a p-Chart
Calculate subgroup proportions
Compute the average of the subgroup proportions
Prepare graphs of the subgroup proportions as a line chart
Compute the upper and lower control limits
Use lines to show the control limits on the p-chart

## Slide 25: p-Chart Example
Subgroup number | Sample size | Number of successes | Proportion, p
1 2 3 … | 150 150 150 | 15 12 17 … | 10.00 8.00 11.33 …
 |  |  | Average subgroup proportion = p

## Slide 26: Average of Subgroup Proportions
The average of subgroup proportions = p
where:
pi = sample proportion for subgroup i
k = number of subgroups of size n
where:
ni = number of items in sample i
ni = total number of items
sampled in k samples
If equal sample sizes:
If unequal sample sizes:

## Slide 27: Computing Control Limits
The upper and lower control limits for an p-chart are
UCL = Average Proportion + 3 Standard Deviations
LCL = Average Proportion – 3 Standard Deviations

## Slide 28: Standard Deviation of Subgroup Proportions
The estimate of the standard deviation for the subgroup proportions is:
If equal sample sizes:
If unequal sample sizes:
where: = mean subgroup proportion
n = common sample size
Generally, is computed separately for each different sample size

## Slide 29: Computing Control Limits
The upper and lower control limits for the p-chart are:
(continued)
Proportions are never negative, so if the calculated lower control limit is negative, set LCL = 0

## Slide 30: c-Chart

## Slide 31: c-Chart
Control chart for number of nonconformities (occurrences) per sampling unit (an area of opportunity)
  Also a type of attribute chart
Shows total number of nonconforming items per unit
  examples: number of flaws per pane of glass
  number of errors per page of code
Assume that the size of each sampling unit remains constant

## Slide 32: Mean and Standard Deviation for a c-Chart
The mean for a c-chart is:
The standard deviation for a c-chart is:
where:
xi = number of successes per sampling unit
k = number of sampling units

## Slide 33: c-Chart Control Limits
The control limits for a c-chart are:

## Slide 34: Process in and out of control

## Slide 35: Using Control Charts
Control Charts are used to check for process control
H0: The process is in control
    i.e., variation is only due to common causes
HA: The process is out of control
    i.e., special cause variation exists
If the process is found to be out of control, steps should be taken to find and eliminate the special causes of variation

## Slide 36: Process In Control
Process in control: points are randomly distributed around the center line and all points are within the control limits
UCL
LCL
time

## Slide 37: Process Not in Control
Out of control conditions:
One or more points outside control limits
Nine or more points in a row on one side of the center line
Six or more points moving in the same direction
14 or more points alternating above and below the center line

## Slide 38: Process Not in Control
One or more points outside control limits
UCL
LCL
Nine or more points in a row on one side of the center line
UCL
LCL
Six or more points moving in the same direction
UCL
LCL
14 or more points alternating above and below the center line
UCL
LCL

## Slide 39: Out-of-control Processes
When the control chart indicates an out-of-control condition (a point outside the control limits or exhibiting trend, for example)

## Slide 40: Out-of-control Processes
  Contains both common causes of variation and assignable causes of variation
  The assignable causes of variation must be identified
    If detrimental to the quality, assignable causes of variation must be removed
    If increases quality, assignable causes must be incorporated into the process design

## Slide 41: Reference Videos
  Honda Statistical Process Control

## Slide 42: Process Capability Measures

## Slide 43: Process Capability Ratio
Cp = tolerance range/process range
= (upper specification limit-lower specification limit)/6σ

## Slide 44: Process Capability Index
Cpi = select lower value
(X(bar) – lower specification)/3σ
(upper specification- X(bar)/3σ

## Slide 45
End
T2LM4
Regents Park Publishers