## Slide 1
Operations Management
Reliability and Redundancy
Regents Park Publishers
T2LM5

## Slide 2
System Reliability

## Slide 3: Learning Objectives
Determine system reliability
Describe how to change system reliability
Determine mean time between failures (MTBF)
Distinguish between reliability of products and reliability of services

## Slide 4: Reliability of Products
Reliability is the probability that a product will function properly for a specified period of time:
Overall Reliability can be adjusted by:
  changing reliability of individual components
  building-in redundancy
  characteristics of a specific design

## Slide 5: Reliability of Services
Reliability of Services is accomplished by:
  Standardization
  Selection and training of employees
  Continuous improvement process
The methods used to change reliability of products cannot be used as methods to adjust reliability of services

## Slide 6
Overall System Reliability

## Slide 7: System Reliability
Systems are built by connecting components:
  in sequence
  in parallel
  as a combination of both
The Overall System Reliability will depend on:
  reliability of each component
  number of components in the system
  arrangement of components (sequential, parallel, or hybrid) in the design

## Slide 8: Overall Sequential System Reliability
Reliability of the system (percent)
Average reliability of each component (percent)
| | | | | | | | |
100 99 98 97 96
100 –
80 –
60 –
40 –
20 –
0 –
n = 10
n = 1
n = 50
n = 100
n = 200
n = 300
n = 400
The Overall Sequential System Reliability will decrease with the increase in the number of components in the system.

## Slide 9
Sequential System Reliability

## Slide 10: Sequential System Reliability
The reliability of the sequential system is a function of the reliabilities of individual components:
Rs = R1 * R2 * R3 * … Rn
where R1 = reliability of component 1
R2 = reliability of component 2
and so on

## Slide 11: Sequential System Reliability Example
Rs
R3
0.99
R2
0.80
R1
0.90
Reliability of this system is calculated to be:
Rs = R1 * R2 * R3 = 0.90 * 0.80 * 0.99 = 0.713

## Slide 12
Parallel System Reliability
(Redundancy)

## Slide 13: Parallel System Reliability
Parallel systems can be used to improve performance of the sequential systems by adding redundancy.

## Slide 14: Parallel System- Redundancy Example
A redundant process is created by backing up selected components with another components
R1
0.90
0.90
R2
0.80
0.80
R3
0.99
= [0.9 + 0.9(1 - 0.9)] * [0.8 + 0.8(1 - 0.8)] * 0.99
= [0.9 + (0.9)(0.1)] * [0.8 + (0.8)(0.2)] * 0.99
= 0.99 * 0.96 * 0.99 = 0.940
Using the previous example: The reliability has increased from
0.713 to 0.940

## Slide 15
Product Failure Rates
and
Mean Time Between Failures

## Slide 16: Product Failure Rate (FR)
Basic units of measure of reliability are:
  Product Failure Rate (FR)
  Mean Time Between Failures (MTBF)

## Slide 17: Product Failure Rate (FR)
FR(%) = x 100%
Number of failures
Number of units tested
FR(n) =
Number of failures
Number of unit-hours of operating time

## Slide 18: MTBF
1
FR(n)
Mean time between failures:
MTBF =
FR(n) =
Number of failures
Number of unit-hours of operating time

## Slide 19
Example

## Slide 20: Failure Rate (%)
20 air conditioning units designed for use in NASA space shuttles operated for 1,000 hours. One failed after 200 hours and one after 600 hours. Calculate the Failure Rate (%) of these units.
FR(%) = 2/20

## Slide 21: Failure Rate (n) (unit-hours)
20 air conditioning units designed for use in NASA space shuttles operated for 1,000 hours. One failed after 200 hours and one after 600 hours.
FR(n)(u-h) = 2/(20,000-1,200) = 0.000106 failures/unit-hr.
Total available unit -hours in operation = 20*1,000 = 20,000
Total unit-hours not in operation = (800+400) =1,200

## Slide 22: Mean Time Between Failures (MTBF)
20 air conditioning units designed for use in NASA space shuttles operated for 1,000 hours. One failed after 200 hours and one after 600 hours.
MTBF = 1/(0.000106) = 9,434 hrs.
1
FR(unit-hour)
MTBF =

## Slide 23
End
T2LM5
Reliability and Redundancy