## Slide 1
Operations Management
Capacity Planning
Regents Park Publishers
T2LM8

## Slide 2: Outline
Capacity
  Design and Effective Capacity
  Capacity and Strategy
  Capacity Considerations
  Managing Demand
Capacity Planning

## Slide 3: Capacity
The throughput, or the number of units a facility can hold, receive, store, or produce in a period of time
Determines fixed costs (break-even and NPV in decision making)
Determines if demand will be satisfied
Three time horizons
Notes: This slide provides some reasons that capacity is an issue. The following slides guide a discussion of capacity.

## Slide 4: Objectives
No “Bombs” Single Points of Failure
No “Bottlenecks”: process slowdowns
Having right resources, at the right level, at the right time, for the right duration.
Notes: This slide provides some reasons that capacity is an issue. The following slides guide a discussion of capacity.

## Slide 5: Planning Over a Time Horizon
Modify capacity
Use capacity
Intermediate-range planning
Subcontract Add personnel
Add equipment Build or use inventory
Add shifts
Short-range planning
Schedule jobs
Schedule personnel
Allocate machinery
*
Long-range planning
Add facilities
Add long lead time equipment
*
* Limited options exist

## Slide 6: Design and Effective Capacity
Design capacity is the maximum theoretical output of a system
  Normally expressed as a rate
Effective capacity is the capacity a firm expects to achieve given current operating constraints
  Often lower than design capacity
Notes: This slide can be used to frame a discussion of capacity.
Points to be made might include:
- capacity definition and measurement is necessary if we are to develop a production schedule
- while a process may have “maximum” capacity, many factors prevent us from achieving that capacity on a continuous basis.
Students should be asked to suggest factors which might prevent one from achieving maximum capacity.

## Slide 7: Utilization and Efficiency
Utilization is the percent of design capacity achieved
Efficiency is the percent of effective capacity achieved
Utilization = (Actual Output/Design Capacity)*100%
Efficiency = (Actual Output/Effective Capacity)*100%
Capacity Cushion
Capacity Cushion = 100% - Average Utilization Rate (%)

## Slide 8: Bakery Example
Design capacity = 1,200 rolls per hour
Bakery operates 7 days/week, 3 - 8 hour shifts
Design capacity = (7 x 3 x 8) x (1,200) = 201,600 rolls
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 9: Bakery Example
Actual production last week = 148,000 rolls
Design Capacity = 201,600 (from the previous slide)
Utilization = Actual Production/ Design Capacity
Utilization = 148,000/201,600 = 73.4%
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 10: Bakery Example
Actual production last week = 148,000 rolls
Effective capacity = 175,000 rolls
Overall Efficiency = 148,000/175,000 = 84.6%
Overall Efficiency = Actual Production/Effective Capacity
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 11: Bakery Example
Effective capacity = 175,000 rolls
Efficiency of new line = 75%
Expected Output =
(Effective Capacity)(Efficiency of New line)
= (175,000)(.75) = 131,250 rolls
Notes: It might be useful at this point to discuss typical equipment utilization rates for different process strategies if you have not done so before.

## Slide 12: Managing Demand
Demand exceeds capacity
  Curtail demand by raising prices, scheduling longer lead time
  Long term solution is to increase capacity
Capacity exceeds demand
  Stimulate market
  Product changes
Adjusting to seasonal demands
  Produce products with complimentary demand patterns

## Slide 13: Economies and Diseconomies of Scale
Economies of scale
Diseconomies of scale
25 - Room Roadside Motel
50 - Room Roadside Motel
75 - Room Roadside Motel
Number of Rooms
25
50
75
Average unit cost
(dollars per room per night)
Henry Ford example

## Slide 14: Capacity Considerations
Forecast demand accurately
Understanding the technology and capacity increments
Find the optimal operating level (volume)
Build for change

## Slide 15: Tactics for Matching Capacity to Demand
Making staffing changes
Adjusting equipment and processes
  Purchasing additional machinery
  Selling or leasing out existing equipment
Improving methods to increase throughput
Redesigning the product to facilitate more throughput

## Slide 16: Complementary Demand Patterns
4,000 –
3,000 –
2,000 –
1,000 –
J F M A M J J A S O N D J F M A M J J A S O N D J
Sales in units
Time (months)
By combining both, the variation is reduced
Snowmobile sales
Jet ski sales

## Slide 17
Operations Management
End
T2LM8